## Slide 1: RS-3/9 HDLC Service
2015. 11. 11
Inter-m

## Slide 2
Tool list
Upload procedure
Contents

## Slide 3
1. Tool list
Upload tooss
LAPTOP

## Slide 4
2. Procedure
1.
LAPTOP
USB
+5V
DVR

## Slide 5
2.. Run AVR stdudio.
2. Procedure

## Slide 6
3) Firmware Download .
Click Icon.
Platform is select AVRISP mkII
And press Connect.

## Slide 7
4) Reset moc.
Device and Signature Bytes selected
ATmega162 then click Erase Device
125 khz Press Write.

## Slide 8
5) Fuse setting.
SPIEN is only checked.
Select Program and Verify
Ext. Crystal Osc. 8.0 –
MHz; Start-up time: 258 CK + 65 ms

## Slide 9
6) Lock Bits 설정합니다.
Press Program and Verify .

## Slide 10
7) Advanced 설정합니다.
Read and Write.
Address가 0x04

## Slide 11
8) Program을 다운로드 합니다.
Erase .
HDLC.hex .
Program Verify .

## Slide 12
● The End ●